## Slide 1
Sub-task ID | Sub-task description | Professional‘s comment | Amount of sub-tasks per Task
pull | pull box on table | Lunge, feet hip wide, chest out, straight back, lean forward, bend front knee, extend your arms, pressure on front leg, pull box by activating back muscles | 4
push | push box on table | Lunge, feet hip wide, chest out, straight back, lean forward, bend front knee, extend your arms, pressure on front leg, push box by activating back muscles | 4
turn | turn box by 90° on table | Feet hip wide, lean slightly forward with straight back, turn box with arm muscles | 4
fold | put the box from one side to another on the table | Feet hip wide, straight back, slightly bended arms, depending on the distance to the box: lean over table, no bended knees, weight of the box remains on the table | 4
carry | translation in space with the box in hand | Chest out, straight back, elbows bended on nearly 90°, box near to body | 4
walk | translation in space without the box | “normal walking on their own judgment“ | 4
lift | lift up the box from the flor | Approach box as near as possible, weight shifted slightly to the front, bend knees, open legs while going down, stop at the raised heels, lean forward with straight back, lift box with quadtriceps in tights, chest out, ellbows aim at ca. 90° | 3
lower | Lower box to flor | Head above pelvis, bend knees and open legs kopf über becken beim aufstehen, kknie beugen und öfnen, brust raus, kopf gerade, gerader rücken | 3
place | put box on table | knie beugen, leicht nach vorne beugen, ame setzen box ab | 2
pick | pick up bock from table | box weit weg dann ausfallschritt, box nah, dann in die knie und paralele füße | 2
 |  |  | Total: 34

## Slide 2
Task 1 |  |  | Task 2 |  |  | Task 3 |  | 
Sub- task# | Description | ST ID | Sub- task# | Description | ST ID | Sub- task# | Description | ST ID
 | start in front of mirror, box on floor |  |  | start in front of mirror, box on floor |  |  | start in front of mirror, box on floor | 
ST1 | lift up box | lift | ST1 | lift up box | lift | ST1 | lift up box | lift
ST2 | carry box to table | carry | ST2 | carry box to scale | carry | ST2 | carry box to table | carry
ST3 | place box on table | place | ST3 | lower box to scale | lower | ST3 | place box on table | place
ST4 | push box away | push | ST4 | lift up box | lift | ST4 | fold box away | fold
ST5 | fold box away | fold | ST5 | carry box to table | carry | ST5 | walk to table center | walk
ST6 | walk to left side of the table | walk | ST6 | place box on table | place | ST6 | turn box left | turn
ST7 | fold box to bottom | fold | ST7 | push box away | push | ST7 | fold box to bottom | fold
ST8 | pull box | pull | ST8 | walk to right side of table | walk | ST8 | push box away | push
ST9 | pick up box | pick | ST9 | pull box | pull | ST9 | walk to right side of table | walk
ST10 | carry box to scale | carry | ST10 | push box away | push | ST10 | pull box | pull
ST11 | lower box to scale | lower | ST11 | walk to table center | walk | ST11 | fold box away | fold
ST12 | lift up box from scale | lift | ST12 | fold box left | fold | ST12 | turn box right | turn
ST13 | carry box to table | carry | ST13 | turn box right | turn | ST13 | push box away | push
ST14 | place box on table | place | ST14 | fold box to bottom | fold | ST14 | walk to table center | walk
ST15 | turn box left | turn | ST15 | turn box left | turn | ST15 | fold box to bottom | fold
ST16 | push box away | push | ST16 | push box away | push | ST16 | turn box left | turn
ST17 | pull box | pull | ST17 | turn box left | turn | ST17 | pick up box | pick
ST18 | turn box right | turn | ST18 | pull box | pull | ST18 | carry box to scale | carry
ST19 | fold box away | fold | ST19 | fold box away | fold | ST19 | lower box to scale | lower
ST20 | pull box | pull | ST20 | turn box right | turn | ST20 | lift up box from scale | lift
ST21 | walk to left side of table | walk | ST21 | walk left side | walk | ST21 | lower box to scale | lower
ST22 | pull box | pull | ST22 | pull box | pull | ST22 | lift up box from scale | lift
ST23 | turn box right | turn | ST23 | fold box to bottom | fold | ST23 | carry box to table | carry
ST24 | push box away | push | ST24 | push box away | push | ST24 | place box on table | place
ST25 | fold box to buttom | fold | ST25 | walk to table center | walk | ST25 | push box away | push
ST26 | push box away | push | ST26 | pull box | pull | ST26 | pull box | pull
ST27 | walk to scale | walk | ST27 | pick up box | pick | ST27 | turn box right | turn
ST28 | walk to box on table | walk | ST28 | place box on table | place | ST28 | walk to right side of table | walk
ST29 | turn box left | turn | ST29 | pick up box | pick | ST29 | pull box | pull
ST30 | pick up box | pick | ST30 | carry box to scale | carry | ST30 | push box away | push
ST31 | carry box to (invisible) mirror | carry | ST31 | lower box to scale | lower | ST31 | pull box | pull
ST32 | put box on floor | lower | ST32 | lift up box | lift | ST32 | pick up box | pick
ST33 | lift box up | lift | ST33 | carry box to (invisible) mirror | carry | ST33 | carry box to (invisible) mirror | carry
ST34 | put box to ground | lower | ST34 | lower box to ground | lower | ST34 | lower box to ground | lower

## Slide 3
Logging ID | Description | Unit | Research question
Elapsed time | Time since the beginning of the task | Milliseconds | RQ1.1.1-3
Current animation Frame | Current frame of the GV animation | frames | RQ1.1.1-3
Subtask ID | The current sub task performed by L | STID | RQ1.1.3
Hip distance | ED between hip of the GV and the hip L | Meters | RQ1.1.1
Left hand distance | ED between left hand GV and left hand L | Meters | RQ1.1.1
Right hand distance | ED between right hand GV and right hand L | Meters | RQ1.1.1
Left foot distance | ED between left foot GV and left foot L | Meters | RQ1.1.1
Right foot distance | ED between right foot GV and right foot L | Meters | RQ1.1.1
Head distance | ED between head GV and head L | Meters | RQ1.1.1*
Box distance | ED between box GV and box L | Meters | RQ1.1.2
Hip angle | ED between hip of the GV and the hip L | Degrees | RQ1.1.1
Left hand angle | ED between left hand GV and left hand L | Degrees | RQ1.1.1
Right hand angle | ED between right hand GV and right hand L | Degrees | RQ1.1.1
Left foot angle | ED between left foot GV and left foot L | Degrees | RQ1.1.1
Right foot angle | ED between right foot GV and right foot L | Degrees | RQ1.1.1
Head angle | ED between head GV and head L | Degrees | RQ1.1.1*, RQ1.3
Box angle | ED between box GV and box L | Degrees | RQ1.1.2
L spine bend | RM spine bend of L | Degrees | RQ1.2
L foot distance | RM base of L | Meters | RQ1.2
L squat distance | RM squat distance of L | Meters | RQ1.2
L hip-box distance | RM elbows L | Meters | RQ1.2
GV spine bend | RM spine bend of GV | Degrees | RQ1.2
GV foot distance | RM base of GV | Meters | RQ1.2
GV squat distance | RM squat distance of GV | Meters | RQ1.2
GV hip-box distance | RM elbows GV | Meters | RQ1.2
L looking at | The object L is looking at | LAID | RQ1.3
Pos x | X position for all 12 trackers | Meters | **
Pos y | Y position for all 12 trackers | Meters | **
Pos z | Z position for all 12 trackers | Meters | **
Rot x | X rotation for all 12 trackers | Meters | **
Rot y | Y rotation for all 12 trackers | Meters | **
Rot z | Z rotation for all 12 trackers | Meters | **
Total 146 columns |  |  | 

## Slide 4
Perspective | Speed Mechanic | Multiple Representations
Ego-centric | Yes | No
Exo-centric | No | Yes
Ego & Exo-centric | Yes | Yes
Augmented Exo-centric | Yes | Yes
Ego & Augmented Exo-centric | Yes | Yes

## Slide 5
 | Session 1 |  | Session 2 |  | Session 3 | 
PT | Perspective | Task | Perspective | Task | Perspective | Task
PT1 | Ego | T1 | Exo | T2 | Ego-Exo | T3
PT2 | Ego | T3 | Exo | T1 | Ego-Exo | T2
PT3 | Ego | T2 | Exo | T3 | Ego-Exo | T1
PT4 | Ego & Exo | T3 | Ego | T1 | Exo | T2
PT5 | Ego & Exo | T2 | Ego | T3 | Exo | T1
PT6 | Ego & Exo | T1 | Ego | T2 | Exo | T3
PT7 | Exo | T2 | Ego-Exo | T3 | Ego | T1
PT8 | Exo | T1 | Ego-Exo | T2 | Ego | T3
PT9 | Exo | T3 | Ego-Exo | T1 | Ego | T2

## Slide 6
student
student
guidance
Avatar Representations
Conditions of VIRTUAL support
REAL
VIRTUAL (COPY)
VIRTUAL
guidance
student
EGO-centric
EXO-centric
guidance
student
EGO-centric
EXO-centric
guidance
student
EGO-centric
EXO-centric
guidance
student
EGO-centric
EXO-centric
EGO-centric guidance
EXO-centric guidance
EGO & EXO-centric guidance
Augmented EXO-centric guidance
guidance
student
EGO-centric
EXO-centric
EGO & Augmented EXO-centric guidance

## Slide 7
400
400
Tracking volume
Mirror
Scale
Vive Tracker
Table
Box
50
50
127?
72?
Lighthouse
270?
270?
270?

## Slide 8
400
400
Tracking volume
Table
Posi-tions
Table tight
Table center
Table left
Mirror
Scale
Mirror
Scale
Box